## Slide 1: Week 15
Keel Bone Chicken Project
12/12/2025

## Slide 2: This Week
This week’s progress
PCB Invoice
Selection of PCB Sensors
  Based on Input from Mechanical Engineering
  Finalized Sensor Selections with Diagrams
  Finalized Part Selections with Footprints and Metrics
Creation of Data Logger Executable
  Insights into Permanent Solutions for Data Logging Issue

## Slide 3: PCB Invoice
Effective Shipment Date: 12/11/2025
Needed to purchase some equipment on the side (Not available on Vendor website
  Battery Holder: https://www.digikey.com/en/products/detail/keystone-electronics/504/2745584?utm_campaign=buynow&utm_medium=aggregator&utm_source=snapeda
  Need to Solder manually
PCB Ordered from Procurement Office in POTR

## Slide 4: Selection of PCB Sensors
Based on Input from Mechanical Engineering
Force Gauge:
1.4 m/s Impact Speed Maximum
1-2 MPa Contact Pressure on Bone
Down from ~10 MPa earlier
Strain Gauge:
~5-10% Strain due to Impact
1.42 kg approximated for Hen mass

## Slide 5: Selection of PCB Sensors
Finalized Sensor Selections with Diagrams
Force Sensor (Capacitive Sensor → Charge Amplifier)
  Force Sensor: SingleTact Force Sensor:
    https://5361756.fs1.hubspotusercontent-na1.net/hubfs/5361756/SingleTact%20Documents/SingleTact_Datasheet.pdf
  Charge Amplifier: AD7150:
    https://www.analog.com/en/products/ad7150.html
Figure 1: Diagram of Finalized Force Sensor

## Slide 6: Selection of PCB Sensors
Finalized Part Selections with Footprints and Metrics
Force Gauge
Charge Amplifier
Outside region irrelevant

## Slide 7: Selection of PCB Sensors
Finalized Sensor Selections with Diagrams
Strain Sensor (Resistive Sensor → Wheatstone Bridge)
  Resistive Sensor: C4A-06-125SLA-120-39P
    https://mm.digikey.com/Volume0/opasdata/d220001/medias/docus/696/125SL.pdf
  Charge Amplifier: INA333AIDGKT
    https://www.digikey.com/en/products/detail/texas-instruments/INA333AIDGKT/1888785?
Figure 2: Diagram of Finalized Strain Sensor

## Slide 8: Selection of PCB Sensors
Finalized Part Selections with Footprints and Metrics
Strain Gauge
Charge Amplifier

## Slide 9: Selection of PCB Sensors
Finalized Part Selections with Footprints and Metrics
Strain Gauge
Charge Amplifier

## Slide 10: Creation of Data Logger Executable
Creation of Executable to Run on Mac/Windows
Issues with Data Logging need to be fixed with creation of remote executable
Tested Hosted Website Compatibility with Omosalewa last Friday

## Slide 11: Creation of Data Logger Executable
Creation of Executable to Run on Mac/Windows
Unsure what options are available with PMDs with Agriculture department:
  Android/iOS
Use of embedded iOS development in iOS/Android
  React Native Frameworks
  #1 (Expo Go), #2 (NativeBase/Base44)
Other Data Storage Options:
  Cloud: GitHub (Subscription Required), AWS, Firebase
  Local: Laptop/Server with SQLite for Database
  Hybrid: Local Storage + (8 Hour Period x 3) Cloud Backups
  Executable/App: Installable app logging data locally
    Local iOS development as seen above

## Slide 12: Next Week
Blockers & Next Week’s Work
Hand over PCB to Mechanical + Agriculture Department
  Write up instructions for use
Figure out data storage problem with current executable
Blockers:
Shipment lead time for PCB

## Slide 13: Thank You
Purdue Polytechnic Institute