## Slide 1: Week 17
Keel Bone Chicken Project
12/22/2025

## Slide 2: This Week
This week’s progress
PCB Reordering
  Purchase Request sent to Procurement Office
PCB Design
  Updates to Rev. 4 of PCB Design
  Added Force + Strain Logging
  Several Design Choices to Minimize Area
Data Analysis
  Able to determine chicken movement from PCB
  Need to change some firmware on the Nicla Sense

## Slide 3: PCB Reordering
Purchase Request sent to Procurement Office
Drill files regenerated and issue dealt with with JLCPCB support
Need to call procurement office to ensure the order successfully goes through
May be an issue with the resistors
  2 mm (length) x 1 mm (height) sizing too small for regular PCBA
  May need to switch to 4 mm (length) x 2 mm (height) for our PCB

## Slide 4: PCB Design
Updated Rev. 4 of PCB Design
Design Files + Footprints found and generated
Footprint of added hardware is smaller than anticipated, which is good
Minimal Issues with Routing this time around

## Slide 5: PCB Design
Added Force + Strain Logging
Sensor Circuitry can be seen in the Schematic below…
Added to PCB on the next slide

## Slide 6: PCB Design
Several Design Choices to Minimize Area
Second Smallest Resistors Chosen due to Assembly Issues
Took precautions to minimize taken area
  Space needed for Ribbon/Flat Flex Cables in the Future
  Space needed for power dissipation in the future

## Slide 7: Data Analysis
From the PCB, ~16 minutes 37 seconds of data was logged
  I had originally set the maximum entries to 1000 -> 16:40
  Missing 3 seconds of data is good, likely startup time
  From the data, I was able to run the following data smoothing program:
Able to determine chicken movement from PCB

## Slide 8: Data Analysis
Need to change some firmware on the Nicla Sense
IMU seems to turn off after extended periods of time on battery (20+ minutes)
  Need to look into this issue and see how it can be avoided in the future
  From data collection, I was able to obtain the following plot
  Very visible when the chicken choose to move vs. fly

## Slide 9: Next Week
Blockers & Next Week’s Work
Need to find the suitable battery replacement on the PCB
Work on Hybrid Approach for Data Collection
Fix Issue where Nicla IMU turned off unexpectedly after a prolonged time of data collection
Instruct Agriculture Department (Omosalewa) on what to do with the boards
Get Sample Data on Force Impacts (Small, Medium, Large Impacts)

## Slide 10: Thank You
Purdue Polytechnic Institute